## Slide 1
Power Characteristics of Irregular GPGPU Programs
Jared Coplin and Martin Burtscher
Department of Computer Science

## Slide 2
Introduction
GPU-based accelerators
  Used in high-performance computing
  Spreading in PCs and handheld devices
Power Characteristics of Irregular GPGPU Programs
Power and energy efficiency
  Power heat
  Electric bill and battery life
  50x boost in performance per watt for exascale computing
Important research area
  Need to develop techniques to reduce power and energy
  Have to develop an understanding of the power consumption behavior of regular and irregular programs

## Slide 3
Regular vs. Irregular Algorithms
Irregular
  Control flow and/or memory access patterns are data dependent
  Runtime behavior cannot be statically predicted
  Example: BST
    Values and their order affect the shape of the binary search tree
3
Power Characteristics of Irregular GPGPU Programs
Regular
  Not data dependant
  Can determine dynamic behavior based only on
    Input size (not values)
    Data structure starting addresses
  Example: Matrix-vector multiplication

## Slide 4
Benchmark Programs
LonestarGPU: common, real-world irregular codes
  Barnes-Hut (BH)
  Breadth-first Search (BFS)
  Delaunay Mesh Refinement (DMR)
  Minimum Spanning Tree (MST)
  Points-to-Analysis (PTA)
  Single-Source Shortest Paths (SSSP)
  Survey Propagation (NSP)
Parboil: mostly regular, throughput-computing codes
  Lattice-Boltzmann Method Fluid Dynamics (LBM)
  Two-Point Angular Correlation Function (TPACF)
  Sparse Matrix Vector Multiplication (SPMV)
4
Power Characteristics of Irregular GPGPU Programs
Notes: TPACF - used as a way to measure the probability of finding an astronomical body at a given angular distance from another astronomical body

## Slide 5
Methodology
Power profiles
  Power as a function of time
Figure 1: Sample power profile
Test bed
  K20c compute GPU
  K20 Power Tool
  Three frequency settings: default, 614, and 324
  Multiple program inputs and implementations
5
Power Characteristics of Irregular GPGPU Programs
Active Runtime
Idle Power
Tail Power
    Idle Power
    Tail Power
    Active threshold
    Active Runtime

## Slide 6
Idealized Power Profile
1. GPU receives work
2. Power draw stable
3. All cores finish
Profile can be captured with two parameters: active runtime and average power
Figure 2: Idealized power profile
6
Power Characteristics of Irregular GPGPU Programs

## Slide 7
Regular Codes
Active power not quite constant
Profiles basically follow idealized shape
Power peaks at different levels
Figure 3: Power profile of three regular codes
7
Power Characteristics of Irregular GPGPU Programs

## Slide 8
Irregular Codes
MST and PTA
  Profiles contain many peaks and valleys
  Dynamically changing data dependencies
  No such thing as a standard profile for irregular codes
NSP
  Topology driven
  Exhibits regular power behavior
Figure 4a: Power profile of irregular codes
8
Power Characteristics of Irregular GPGPU Programs

## Slide 9
BFS and SSSP
  Topology driven
  Exhibit regular power behavior
  Lots of unnecessary work
DMR
  Many peaks and valleys
  ~90 seconds of near idle power shows loss of parallelism
BH
  Appears mostly regular
  10k bodies, 10k timesteps
  Irregularity is masked by short runtimes of individual kernels
Irregular Codes (cont.)
Figure 4b: Power profile of irregular codes
9
Power Characteristics of Irregular GPGPU Programs

## Slide 10
BH 100k Bodies, 100 Time Steps
100k bodies, 100 timesteps
  Kernel invocation evident
  Higher average power draw with 100k bodies over 10k bodies (red dashed line)
    10k bodies not enough to fill GPU
  Irregularity within each timestep still not visible
Figure 5: Power profile of BH with 100k bodies and 100 time steps
10
Power Characteristics of Irregular GPGPU Programs

## Slide 11
BH 22M bodies, Single Time Step
11
Power Characteristics of Irregular GPGPU Programs
Decrease due to load imbal.
Two similar irreg. kernels
One more irreg. kernel
Very short regular kernel
Regularized main kernel

## Slide 12
Idealized-Regular-Irregular
Idealized and Regular
  Similar shapes
Irregular
  Obviously different
    Load imbalance
    Memory access patterns
    Control flow
  Power fluctuates wildly
    Averages 82W
    From high to low, 60% difference
  Cannot be accurately captured by averages
Figure 6: Comparison of idealized, regular, and irregular profiles
12
Power Characteristics of Irregular GPGPU Programs

## Slide 13
Different Implementations of BFS
WLA
  Topology driven
  Lowest avg power and peak power
Atomic
  Fastest topology driven version
  Irregular power profile
WLC and WLW
  Data driven
  Irregularity is masked by short runtimes
Shape of the profile depends on implementation strategy
Figure 7: Profile of different implementations of BFS
13
Power Characteristics of Irregular GPGPU Programs

## Slide 14
SSSP with Different Frequencies
Topology driven implementation
Same input (roadmap of USA)
Default setting
  705 MHz core; 2600 MHz memory
614
  614 MHz core; 2600 MHz memory
  Energy stays about the same
324
  324 MHz core; 324 MHz memory
  Energy increases
  Terrible for memory bound codes
Figure 8: Profile of SSSP on different frequencies
14
Power Characteristics of Irregular GPGPU Programs

## Slide 15
PTA with Different Inputs
Distinctly different profiles
  Pine averages 15 W more than vim
  Tshark has initial spike followed by a 1.5 second valley before ramping up
  Pine and vim have more spikes and ramp down slightly over time
Cannot use a profile from one input to characterize the power draw over time of another
Figure 9: Profile of PTA for different inputs
15
Power Characteristics of Irregular GPGPU Programs

## Slide 16
Summary
Regular codes often similar to idealized
Irregular Codes
  No such thing as a standard power profile
  Implementation and input can greatly affect power profile
  Early behavior may not be indicative of later behavior
  Cannot easily be captured by averages
Power over time
  Must be considered
  Re-evaluated for each input and any code modification
  Provides understanding of software effects on hardware
16
Power Characteristics of Irregular GPGPU Programs

## Slide 17
The work reported herein is supported by:
U.S. National Science Foundation
  DUE-1141022
  CNS-1217231
  CNS-1406304
  CCF-1438963
Texas State University
NVIDIA Corporation
17
Power Characteristics of Irregular GPGPU Programs
Questions